## Slide 1: TITO EF5 Simulation/Ouputs info

## Slide 2: First Run
We Start with warmup states or run a warmup for 3 months to 1 year.
We always save the states at the latest IMERG which comes with a delay of 4 hours.
We fill the delay from -4hour(last latest IMERG) till the current time/simulation time with nowcasting Convolutional LSTM (ConvLSTM).
We then switch to Forecast/Long Range mode using GFS and run a forecast till +24 hours.

## Slide 3: Second Run
From the next runs we start from the saved states from the last run, at this point we get 1 hour of new IMERG.
We again save the states at -4 hour on the latest IMERG.
Rest everything is same.

## Slide 4: Second Run
From the next runs we start from the saved states from the last run, at this point we get 1 hour of new IMERG.
We again save the states at -4 hour on the latest IMERG.
Rest everything is same.

## Slide 5: Outputs
  Each Simulation produces the below outputs
  Max Unit Stream Flow (m³/Sec/Km²).
  Max Stream Flow (m³/Sec).
  Max Soil Moisture (0 – 100 %).
  QPE: Quantitative Precipitation Estimation accumulated (via IMERG + Nowcasting).
  QPF: Quantitative Precipitation Forecast accumulated (via GFS).
  Max Depth: Inundation

## Slide 6: Geo Tiffs Metadata
  Each Geotiff consist of meta data
  Metadata consist of simulation begin and end date timestamp
  Example for a simulation run at 202606101600 has:
  Start – 202606101100
  IMERG_End – 202606101600
  GFS_Begin - 202606101600
  End – 202606112200
  Meta data from
  Max Unit Stream Flow

## Slide 7: Geo Tiffs Metadata
  Meta data from :
  Max Unit Stream Flow
  QPE Accum (Coming from IMERG + Nowcasting)
QPF Accum (Coming from GFS)

## Slide 8: Geo Tiffs Metadata
  Each Geotiff consist of meta data
  Metadata consist of simulation begin and end date timestamp
  Example for a simulation run at 202606101600 has:
  Start – 202606101100
  IMERG_End – 202606101600
  GFS_Begin - 202606101600
  End – 202606112200
  Meta data from
  QPE Accum (Coming from IMERG + Nowcasting)

## Slide 9: Timeseries
  In the outputs we also get timeseries across below selected locations in the form of csv’s

## Slide 10: Timeseries
  Each CSV contains the below information
  Time Stamp
  Discharge
  Observed (not applicable)
  Precipitation
  PET
  Fast Flow
  Slow Flow